## Slide 1: Signalized Intersection Delay Monitoring for Signal Retiming
SafeTrip-21
Safe and Efficient Travel
through Innovation and Partnership in the 21st Century
Sudhir Murthy, PE, PTOE
President
TrafInfo Communications, Inc.
Lexington, MA

## Slide 2: Presentation Outline
System Objectives
Methodology
Technology
Test Site
  Equipment Installation
  Data Collected
Results
Concluding Remarks

## Slide 3: System Objectives
To monitor traffic operations at a signalized intersection in real-time (cycle-by-cycle) by:
  Collecting traffic signal timing and volume data
  Estimating control delay using procedure within the 2000 Highway Capacity Manual (HCM)
To develop a cost-effective system to
  Identify signalized intersections in need of improvements (ex. Re-timing)
  Allow remote download of new signal timing
  Assess the benefits resulting from it

## Slide 4: Methodology
HCM Control Delay
where
g = effective green (sec)
C = cycle length (sec)
v = volume
S = saturation flow rate
PF = Progression Adjustment Factor
(Exhibit 16-12 using Arrival Type)
Directly measured
Estimated from
Directly measured
Headway & Occupancy
HCM Procedure
k = Incremental delay factor
(Exhibit 16-13)
I = Upstream filtering factor
(assumed = 1.0)
d1 = uniform delay d2 = incremental delay
d3 = initial queue delay

## Slide 5: Technology
Trafmate™ 6
Integrated C-programmable micro-controller with dual serial port and wireless PCS cellular modem
GTT Canoga ™ Loop Detector
Traditional loop detector with count capability (including “long loop”) and a front panel serial port

## Slide 6: Test Site
El Camino Real
at Dumbarton Rd/Oakland St
Redwood City, CA
Φ1
Φ6
Φ4
Φ4
Φ5
Φ2
N

## Slide 7: Test Site Assessment
Thorough assessment of each loop in terms of inductance waveforms
Calibration of Canoga loop detector parameters for “long-loop” counting

## Slide 8: Long Loop Detection Technology
Car 1
Car 2

## Slide 9: Test Site Installation
BEFORE
AFTER
Signal
Timing
Traffic
Volume

## Slide 10: Data Collected
Signal Timing
  Total cycle length
  Green time of each phase
Traffic Volume
  Time to service first vehicle in queue
  Volume during green & clearance
  Total occupancy during green
  Average headway (from 3rd to 10th vehicle)
Central
Server
Software
MySQL®
Database
Web-Interface
Control Delay
User
Wireless
Internet

## Slide 11: Results - Control Delay
Southbound Through Lane 1
Northbound Exclusive Left Lane

## Slide 12: Unique Aspects of System
Estimation of Saturation Flow Rate of each cycle from headway measurements
Estimation of Arrival Type using occupancy and volume measurements

## Slide 13: Direct Field Measurement of SFR
1
2
3
4
5
6
7
8
9
10
1
2
3
4
5
6
7
8
9
10
3
4
5
6
7
8
9
10
11
11
Headway measurements
11
12
12

## Slide 14: HCM Saturation Flow Rate Calcs

## Slide 15: Project Results – Saturation Flow Rate
Estimated based upon headway – SB Thru Lane 1
Default: Values computed using HCM
Default: Values computed using HCM

## Slide 16: HCM Arrival Types

## Slide 17: Occupancy-Arrival Type Relationship
Arrival Type
Occupancy
0%
100%
1
2
3
4
5
6
Actual
Field
Measurement
Estimated

## Slide 18: Project Results - Arrival Type
Estimated based upon occupancy and volume – SB Thru Lane 1

## Slide 19: Steps to Retime Signals
Collect data for 2-3 days and evaluate data to determine need for signal timing
Use volume information to determine optimal signal timing (ex. Synchro, etc)
Upload new signal timing to controller via the wireless modem
Continue to collect data for another 2-3 days and evaluate data.
Repeat steps if necessary or document improvements.

## Slide 20: Concluding Remarks
Demonstrates a cost-effective method for signalized intersection traffic monitoring
Next Steps:
  Additional reporting capability (ex. Peak hour)
  Real-time adjustments to saturation flow rate and arrival types
Future Challenges:
  Variety of detection systems for signal control
  Data accuracy of detection systems